Project 1
Daniel Christiansen
ECE 171
11/13/14

The focus of this project was to design and test a circuit that displays a single digit in Braille. The circuit was to take in a four-bit BCD digit, and output six bits, representing the Braille digit.

The digit was to be represented as six individual bits of output, symbolizing the six dots that make up a character in Braille. Specifically, we were to design the circuit to display the digits 0 – 9, based on the value of the input.

Since the value corresponding to each digit wasn't specified, it seemed simplest to make the digit match the BCD value. The first step was to create a truth table containing all six outputs as determined by the four bits of the BCD digit. Next, filling out k-maps, and simplifying to obtain six logical functions that could be translated into circuits. I first created the behavioral module in verilog, then mapped out the circuit, then created the structural module after I knew exactly how the parts available would force me to arrange it.

The circuit contains the following parts:

1 X CD74HCT04 6 X Inverter

2 X CD74HCT11 3 X 3-input AND gate

2 X CD74HCT08 4 X 2-input AND gate

2 X CD74HCT32 4 X 2-input OR gate

1 X CD74HCT4075 3 X 3-input OR gate

I chose to design the circuit using cascading gates in several places, so there are several places where there is a higher propagation delay than there might have been had I used OR gates with four inputs. I restricted myself to what I could find listed on the 'logic' section of ti.com.

The highest possible delay in the circuit is the output 'B4', with a maximum delay of 93 nanoseconds.